## Slide 1
Presented by: Larry Gould
Route 30A Autonomous Transit Workshop
Preliminary Findings
February 5, 2020

## Slide 2: AgendA
Route 30A Autonomous Transit Workshop
Transit’s Role on Route 30A
Vehicle Options
Example Transit Cross-Sections
Transit Service Characteristics

## Slide 4: Role of transit on route 30a
Allow residents and employees to avoid congestion
Encourage tourists and visitors to avoid driving to key destinations
Enable employees to get to work without needing a car
Improve sustainability and local air quality by reducing vehicle emissions

## Slide 5: Transit demand segments
Commute trips
Errands and work-related trips
Shopping and social trips
Tourist and beach trips
Medical trips

## Slide 6: Temporal patterns of demand
Commuting peak hours for local jobs (e.g. service-sector workers)
Late-night service to serve bars/restaurants
Year-round service
Peak season for tourism (i.e. April - November)

## Slide 7: Development density and recommended service frequency
Evaluate:
Population density
Employment density
Evaluate transit propensity of key communities:
  Older adults
  Youth
  People with disabilities
  People of color
  People with low incomes
  Zero-vehicle households

## Slide 8: Service design and trip purpose

## Slide 9: Bus Stop Spacing

## Slide 10: Brt designs

## Slide 11: Vehicle Options
Electric on-demand transit (“club car”)
Autonomous electric club car
25’ electric shuttle
30’ transit bus
40’ transit bus
Electric 40’ transit bus
Autonomous electric transit bus (future)

## Slide 12: Electric On-Demand Transit (“Club Car”)
Pros:
Inexpensive vehicles
Zero-emissions
Dedicated drivers (unlike autonomous)
Cons:
May not be ADA compliant
Limited battery range
Lower capacity than most transit buses or shuttles
Models: Polaris GEM, Chevrolet Bolt EV
Useful life: N/A
$15,000 - $30,000

## Slide 13: Autonomous Electric Shuttle
Pros:
Zero-emissions
Lease includes vehicle, insurance, maintenance, driver supervision
Cons:
Typically only operated at speeds below 20 mph (max. is 35 mph), limiting their use on certain corridors
May not be ADA-compliant
Limited battery range (30-60 miles)
Lower capacity than transit buses or shuttles (10-15 pax.)
Models: Navya Arma, EZ10
Useful life: Not yet established
$150,000 per year (lease)

## Slide 14: 25’ Electric Shuttle
Pros:
ADA compliant
Higher capacity than club car
Narrower width (9’) than 40’ transit bus
Cons:
Higher maintenance costs
Manufacturers: New Flyer, Daimler, TransTech, Gillig, Schetky, Volvo
Useful life: 12+ years
$350,000 - $600,000

## Slide 15: 30’ Transit Bus
Pros:
Common to many transit fleets
ADA compliant
Higher capacity than either club car or 25’ electric shuttle
Cons:
Lower capacity than 40’ transit bus
Wider vehicle requires more street space (11’)
Manufacturers: New Flyer, Daimler, TransTech, Gillig, Schetky, ElDorado
Useful life: 12+ years
$450,000 - $600,000

## Slide 16: 40’ Transit Bus
Pros:
Common to many transit fleets
ADA compliant
Higher capacity than either club car or 25’ electric shuttle
Cons:
Higher maintenance costs than electric transit buses
Wider vehicle requires more street space (11’)
Manufacturers: New Flyer, Daimler, TransTech, Gillig, Schetky, Volvo
Useful life: 12+ years
$500,000 - $600,000

## Slide 17: Electric 40’ Transit Bus
Pros:
Zero-emissions and reduced noise
ADA compliant
Higher capacity than transit bus
Cons:
Limited battery range
Highest maintenance costs
Wider vehicle requires more street space (11’)
Manufacturers: Proterra, New Flyer, Green Power, BYD, Smith Electric Vehicles
Useful life: 12+ years
$700,000 - $1 Million

## Slide 18: autonomous Transit Bus
Pros:
Zero-emissions
ADA compliant
Higher capacity than transit bus
Lower operating costs than non-autonomous buses
Cons:
Still in development
Limited battery range
Highest maintenance costs
Wider vehicle requires more street space (11’)
Manufacturers: Mercedes-Benz
Useful life: Not yet established

## Slide 19: Potential Roadway designs
Bidirectional, single transit-only lane in roadway center on south side of 30A

## Slide 20: Potential Roadway designs
Two uni-directional, shared transit/micro-mobility lanes
Image Source: NUE Urban Concepts

## Slide 21: Potential Roadway designs
Two uni-directional, shared transit/micro-mobility lanes
Image Source: NACTO

## Slide 23: Bus priority

## Slide 24: Transit Signal Priority

## Slide 25: Queue Jump Lanes
Image Source: AC Transit

## Slide 26: Potential bus stop designs
Boarding bulb stop

## Slide 27: Potential bus stop designs
Curbside Pull-out stop
Image Source: NACTO

## Slide 28: Potential bus stop designs
Side boarding island stop

## Slide 29: Potential bus stop designs
Park-and-ride

## Slide 30: Potential bus stop designs
Park-and-ride

## Slide 31: Potential bus stop designs
Median Stop, Right-Side Boarding
Image Source: NACTO

## Slide 32: Potential bus stop designs
In-Lane Sidewalk Stop
Image Source: NACTO

## Slide 33: Potential Daily Ridership
Transit Mode Share | Average Daily Traffic (ADT): 12,000 | Average Daily Traffic (ADT): 18,000
5% | 600 | 900
10% | 1,200 | 1,800
20% | 2,400 | 3,600
30% | 3,600 | 5,400

## Slide 34: Potential fare structure
Fare-free
Fare, with off-board fare payment to reduce bus dwell time

## Slide 35: Role of Transportation demand management (TDM)
Demand management
  Commuter benefits incentives to encourage sustainable modes (e.g. free transit passes for employees)
  Transit-oriented development
  Form-based codes
  Reduced minimum parking requirements
  Pricing of public parking
  Expansion of bike, pedestrian facilities (e.g. bike share, scooters)
Supply management
  Joint-use/shared parking agreements
  Public/private parking agreements

## Slide 36
646.274.3725
lgould@nelsonnygaard.com
Larry Gould

## Slide 37
PNG Originals: O:\software tools\Icons\NN Icons PNGs

## Slide 38
PNG Originals: O:\software tools\Icons\NN Icons PNGs